## Slide 1: Determination of Method Validity of Identifying the Presence of Titanium Dioxide in Commercial Pool Care Products via Raman Spectroscopy
Research and presentation by Maddie Hubbard, Dylan VanSpankeren, Jessica Whitehouse

## Slide 2: Objective
The initial goal of this experiment was to determine the concentration of TiO2 in the commercial pool care product Solei Sun Powered Water Care.
This goal then developed into the determination of method validation of identifying TiO2 in Solei Sun Powered Water Care as the experiment progressed.

## Slide 3: Background
The real sample tested is a patent pending pool care product. The analyte, TiO2, is what makes this product special as it aims to reduce the levels of chlorine in household pools
The exact concentrations are not listed which led us to wanting to try and determine the concentration of TiO2 ourselves
TiO2 is a commonly used chemical for colouring products white. It is used in products such as paints, plastics, paper, and soaps
Raman was the instrument of choice as it is powerful at detecting specific structures along with its short run time

## Slide 4: Instrument Specifications
Raman Spectrophotometer (Anton Paar Cora 5001)
  785nm wavelength
  250s exposure time
  450mW laser power

## Slide 5: Experimental: Week 1
Created two stocks with TiO2 powder and water
Stock 1
  Vortexed and sonicated
  Appeared white, opaque, and grainy
  See right side of figure
  Filtered through 0.45µm luer lock
  686ppm
Stock 2
  Thoroughly hand-shaken
  See left side of figure
  26ppm

## Slide 6: Week 1 Cont’d
Blank sample contained water
This run was subtracted from future runs
Real sample was run
Once as undiluted
Once spiked with 3.5mL stock 1 in 10mL flask
Once spiked with 5mL stock 2 in 10mL flask
Once spiked with 1mL stock 2 in 100mL flask

## Slide 7: Tables for Concentrations: Week 1
Stock Solution | Mass of Solid TiO2 (g) | Volumetric Flask Used (mL) | Concentration (ppm)
1 | 0.0343 | 50 | 686
2 | 0.0026 | 100 | 26
Dilute Stock Solution | Diluted from Stock Solution # | Volume of Stock Solution Used (mL) | Volumetric Flask (mL) | Concentration (ppm)
3 | 1 | 3.5 | 10 | 240
4 | 2 | 5.0 | 10 | 13
5 | 2 | 1.0 | 100 | 0.26

## Slide 8: Week 2
A stock with 3.7mg TiO2 powder in a 250mL flask was prepared (15ppm)
This was used to prepare nine standards, mixed with real sample, in a standard addition fashion
Each standard was run once, along with a water blank which was subtracted

## Slide 9: Week 2 Cont’d
The real sample was also directly spiked with the TiO2 powder in 250mL volumetric flasks with varying masses
  Less than 4.7mg
  4.7mg
  27.9mg
These spiked samples were filtered through 0.45µm luer lock

## Slide 10: Tables for Concentrations: Week 2
Standard | Real Sample Volume (mL) | TiO2 Stock Solution (mL) | Deionized Water (mL)
1 | 10 | 0 | 40
2 | 10 | 5 | 35
3 | 10 | 10 | 30
4 | 10 | 15 | 25
5 | 10 | 20 | 20
6 | 10 | 25 | 15
7 | 10 | 30 | 10
8 | 10 | 35 | 5
9 | 10 | 40 | 0
Spiked Real Sample | Mass of Solid TiO2 (mg) | Volume of Real Sample (mL) | Position (cm-1) | Peak Height (a.u.)
1 | 4.70 | 250 | 129.57 | 267.42
2 | 27.9 | 250 | 129.68 | 145.29
3 | <4.70 | 250 | 129.82 | 187.53

## Slide 11: Data and Results
While this was not a quantitative experiment, an analysis of the spectra can show the validity of the method

## Slide 12: Filtered Real Sample

## Slide 13: Spiked with less than 4.7mg

## Slide 14: Spiked with 4.7mg

## Slide 15: Spiked with 29.7mg

## Slide 16: Conclusion
This experiment involved constant trial and error to get consistent results from the samples
The TiO2 proved difficult to work with as it is a very powerful dye and does not dissolve well
The final method of spiking the sample directly with the powder proved to have the most validity to it
By doing this the peak correlating to TiO2 grew in height. The overall solution colour remained constant after filtering suggesting there is a process occurring in the real sample to remove solid TiO2 pieces

## Slide 17: Future Work
Future work would involve the continuation of method development to a point that would allow for the initial goal to be achieved.
Since there was increasing peak heights as the amount of stock sample added changed, this leads us to believe there is merit to this method.
Another option would be exploration of other solvents to dissolve TiO2. This would require more work dealing with different matrixes but could prove useful